| SR. NO. | TOPIC NAME |
| --- | --- |
| 1 | Introduction |
| 2 | Selection Of Topic |
| 3 | What Is Black Cotton Soil |
| 4 | Soil Reports |
| 5 | Quality Of Black Cotton Soil |
| 6 | Methods Of Improving Quality Of Black Cotton Soil |
| 7 | Types Of Bridge |
| 8 | Components Of Bridge |
| 9 | Scour Depth |
| 10 | Design Of Abutment |
| 11 | Types Of Foundation |
| 12 | Problems Detected In Foundation |
| 13 | Foundation Design Process |
| 14 | Precautions Have To Be Taken While Make The Structure On Soft Soil |
| 15 | Granular Pile-Anchor Foundation System |
| 16 | Rehabilitation Of Distressed Structure Founded On Expansive Soil |
| 17 | Failure Case |
| 18 | Compaction Characteristics |
| 19 | Strength Characteristics |
| 20 | Foundation Practice And Rehabilitation Of Structure On Expansive Soil |
| 21 | Design Of Components |
| 22 | Groundnut Shell Ash Stabilization Of Black Cotton Soil |
| 23 | Conclusions |
| 24 | References |

INTRODUCTION

- We have to done the project in 5th & 6th semester from the reference of the                                                                                                                                                                                                                site constructed at. Parab Haldaru kamrej, Surat.

- In 5th semester we define the problems occur during the construction of foundation of bridge on black cotton soil.

- And in 6th semester we have to define the problem’s  solution  and remedial measure for detected problems during construction.

- How to construct the foundation on black cotton soil that we have to define, and also design the foundation.

Selection Of Topic

- According to this project the foundation of bridge is maximum chances of  failure on black cotton soil because of its characteristic are as below,

- If black cotton soil get any kind of moisture then it will be shrinkage  immediately.

- Mostly in summer the soil will be dry then cracks are developed on the surface of the soil.

- The load bearing capacity of black cotton soil is less.

- Water cannot be pass through from black cotton soil.

- The failure of bridge  foundation cause on black cotton soil is,

- Sinking of foundation

- Collapse of foundation

- Settle down of foundation

- So , because of characteristic of black cotton soil the foundation of bridge  should be especially design for the safety.

What Is Black cotton Soil ?

BC soils  absorb water heavlly , swell, become soft, lose strength, easily and has atendency to heave during wet condition.

Quality Of Black cotton Soil :

- BC soils absorb water heavlly, swell, become soft, lose strength, easily and has atendency to heave during wet condition.

- BC soils shrink in volume and develop cracks during summer. They are by extreme hardness and cracks when dry.

- Soils are called highly expansive when free swell index exceeds 50 undergo volumetric changes leading to pavement distortion, crakin unevenness due to seasonal wetting and drying.

- BC soils produce a CBR value of 2 to 5% if compacted efficiently.

Method Of Improving Quality OF Black Cotton Soil

- To limit the load on the soil to 5.5 tonnes/ sq.mt. if water is liable to find an access to the foundations, the limit of loading should be restricted to 4.9tonnes/ sq.mt.

2. To take the foundation to such depths where the cracks cease to extend.The minimum depth of foundation should be not Less than 1.5 mt.

## Under-Reamed Piles

Under-reamed bored piles were introduced in India by Central Building Research Institute (C.B.R.I), Roorkee. In India, at about 3.5m below the ground, movements are negligible and if foundations are anchored at that depth, they will remain stable. Based on this principle, under-reamed piles (Sharma et al, 1978) were adopted for foundations in expansive soils in India. The bulbs are provided generally in the inactive zone where sufficient anchorage is available. The diameter of the stem of the under-reamed pile ranges from 20-50cms and the diameter of the bulb is normally 2 ½ times the diameter of the stem. The spacing of the bulbs, in the case of multi under-reamed pile, should not exceed 1 ½ times the bulb diameter. The Bureau of Indian Standards has also brought a code IS 2911: Part III-1980 on under-reammed piles.

Under-Reammed Pile Foundation      Granular Pile-Anchor Foundation System

Types Of Bridge :

- According to the flexibility of superstructure as fixed span bridges or movable bridges.

- Fixed span superstructure

In case of fixed span superstructure, the superstructure remains in a fixed position and most of the bridges are of this category.

- Movable span bridges

In case of movable span superstructure, the superstructure is lifted or moved with the help of some suitable arrangement.

- According to the position of bridge floor relative to the formation level and the highest flood discharge as deck bridges, through bridges or semi through bridges.

- Deck bridges

Deck-type bridges refer to those in which the road deck is carried on the top flange or on top of the supporting girders. The deck slab or sleeper may cantilever out to some extent beyond the extreme longitudinal girder.

- Through bridges

In the through type bridges, the decking is supported by the bottom flange of the main supporting girders provided on either side.

- Semi through bridges

The semi-through bridge has its deck midway and the deck load is transmitted to the girder through the web of the girder. In this also, the main girders are on either side of deck.

- According to the inter-span relations as simple, continuous or cantilever bridges.

- Simply supported

Generally width of bridge is divided into number of individual spans. For each span, the load carrying member is simply supported at both ends.

The plate girder and truss girders are used as this type of bridges. They are suitable at places where uneven settlements of foundations are likely to take place.

- Continuous

In continuous bridges spans are continuous over two or more supports. They are statically indeterminate structures. They are useful when uneven settlement of supports does not take place. In continuous bridges the bending moment anywhere in the span is considerably less than that in case of simply supported span. Such reduction of bending moment ultimately results in the economic section for the bridge. In continuous bridges the stresses are reduced due to negative moments developed at pier or supports. Thus continuous span bridges have considerable saving compared to simply supported bridge construction. Following are the advantages of RCC continuous girder bridges over simply supported girder bridges.

- As the bearings are placed on the centerline of piers, the reactions at piers are transmitted centrally.

- It is found that the continuous girder bridge suffers less vibration and deflection.

- The continuous girder bridge requires only one bearing at each pier as against two bearing for simply supported girder bridge.

- The depth of decking at mid span is reduced and it may prove to be useful for over bridges where headroom is of prime consideration.

- The expansion joints required will be less.

- There is reduction in cost as less quantity of concrete and steel are required.

- Components of bridge

- The bridge structure comprises of the following parts.

- Superstructure or Decking

This includes slab, girder, truss, etc. This bears the load passing over it and transmits the forces caused by the same to the substructures.

- Bearings

The bearings transmit the load received from the decking on to the substructure and are provided for distribution of the load evenly over the substructure material which may not have sufficient bearing strength to bear the superstructure load directly.

- Substructure

This comprises piers and abutments, wing walls or returns and their foundation.

- Piers and Abutments

These are vertical structures supporting deck/bearing provided for transmitting the load down to the bed/earth through foundation.

- Wing walls and Returns

These are provided as extension of the abutments to retain the earth of approach bank which otherwise has a natural angle of repose.

- Foundation

This is provided to transmit the load from the piers or abutments and wings or returns to and evenly distribute the load on to the strata. This is to be provided sufficiently deep so that it is not affected by the scour caused by the flow in the river and does not get undermined. While the above mentioned are structurally operational parts, for safety hand rails or parapets, guard rails or curbs are provided over the decking in order to prevent vehicle or user from falling into the stream or for the separation of traffic streams.

- Description

Foundation :

The foundation is the main part of any construction. The stability or the strength of the structure  depends on foundation.

There are different  types of foundations for the different types of soils. There are many types of foundations are in use.

Like ,

- Pile  foundation

- deep foundation

- mat foundation

- cassion foundation

- shallow foundation

This structure is Founded  on black cotton soil. The black cotton soil is a fully saturated with water . so the load bearing capacity of this soil is very low and thus  there are no strong platform on upper level of soil for foundation. As hard strata is available at the depth of 3.50 m and hence minimum depth for foundation should be taken either 3.50m or more.

The whole load of the structure is transmited to the ground via foundation.

The foundation is made of the the concrete and steel. The steel  can provide more strength to the foundation especially for tensile forces and therefore open foundation is used.

This foundation is 3.50 m deep from ground level. M20 Grade  concrete is used  in this foundation and the ratio of this concrete 1:1.5:4.

For the construction there are put the circular cassion in the river  and then after removed the water from that cassion. and then after done the concreteing in that cassion after the setting of the concrete the cassion will be removed and then after get the strong foundation.

Problem detected in foundation :

- Mistakes in checking of load bearing capacity of soil:

- The design of foundation is depended on load bearing capacity of particular types of soils. If engineer created any mistakes to find out load bearing capacity of soil then automatically wrong foundation design is created. Because of that mistake foundation gone a failure…….

- Soil of this site is black cotton soil and load bearing capacity of black cotton soil is less. That’s why open foundation is used here.

- Crack in foundation :

We detect some cracks on foundation of this structure. That cracks is created by using low quality of concrete or do not removing the air voids when during the concreting work.

It is also create because not using the vibrator machine in concreting. Because of vibrator machine the air voids are removed from foundation.

The cracks are also created if setting time given to the concrete is less.

Foundation Design Process :

- Scope & Field Reconnaissance

- Field Explorations & Field Testing

- Laboratory Testing

- Foundation Design

- Foundation Reports

- Specifications

- Construction Support

Specifications:

Piling 
		Estimated Pile Lengths (steel piles)
		Number of Pile Splices
		Tip Treatment (open or closed end, reinforcement)
		Driving Criteria
		Wave Equation Input (if applicable)
		Pile freeze, preboring or jetting allowed

Shafts 
		Designated Friction or End Bearing
		Permanent Casing Requirements
		Crosshole Sonic Log (CSL) testing required

Precautions have to be taken when making the structure on soft soil :

1) Use the deep foundation for structure like pile foundation.

- Pile Design:

- Most Common			
		Steel Pipe Piles (open or closed end)
		H-Piles

- Less Common
		Prestressed Concrete
		Timber

- Bearing Resistance (compression and tension)

- Lateral Resistance

- Settlement and Downdrag Analysis

- Corrosion Potential/Protection

- Tip Protection

- Pile Drivability (construction)

- Group Settlement, Group Effects

2) Providing suitable drainage system for bridge.

3) Make the filter media of rubble for side of abutment of bridge.

4) Design the lightweight superstructure of bridge.

Because if weight of superstructure is low then   load comes on foundation is less.

Points to consider in mind while doing the foundation on Black cotton soil / clay soil.

1)      Always give soil treatment to subgrade before

placement of concrete.

2)    Always apply vibrating  equipment after

placement of concrete.

3)   Mix suitable admixture in concrete . Admixture Give more strength to concrete & reduces cement level i.e low consumption of cement which reduces the cost of constrution.

## Granular Pile-Anchor Foundation (GPAF) System

It has been observed that under-reamed pile foundations suffer from the difficulty of both formation upon which the whole mechanism of anchoring depends. Phanikumar et al (1996) felt that the cost of under-reamed pile foundation is more for light structures where the cost of structure itself is very low. In this technique, the foundation is anchored at the bottom a granular pile to mild steel anchor plate with the help of a mild steel anchor rod. This is called a granular pile-anchor (Fig. 7) also counteracts the problem of shrinkage acting as a storage medium. As the granular pile is a particulate medium, it cannot resist the tensile uplift force on the foundation, and as such needs to be modified into a pile-anchor by the above mechanism. As the expansive soil absorbs water, it swells and uplifts the foundation. But, an enormous resistance to uplift is mobilized along the cylindrical pile–soil interface because of the shear parameters of the Pile-soil Interface, and the shear resistance augmented by the lateral swelling pressure. Model tests conducted in the laboratory revealed that heave and swell potential are enormously reduced by the installation of granular pile anchors. The % reduction was about 90 to 95. It has also been observed that the strength characteristics of the ambient soil surrounding the granular pile-anchor showed a large improvement and that the composite ground showed improved bearing capacity.

## Chemical Stabilization

Chemical stabilization of expansive soils can be adopted to alleviate the problems posed by these soils to civil engineering structures. Chemical stabilization of expansive clays consists of changing the physico-chemical around and inside of clay particles where by the clay requires less water to satisfy the static imbalance and making it difficult for water that moves into and out of the system. The most common chemical admixtures used in soil stabilization are lime and cement.

Lime stabilization has been used successfully on major projects to minimize swelling of the expansive soil. Generally, 3 to 8% by weight hydrated lime is added to the top several inches of the soil (John et al). Lime continues to be widely used additive for modification of expansive clays in view of its cost-effectiveness although limited success in many instances. Lime is sparingly soluble in exchange reactions are less. Further, the lime diffusion into soil either from lime piles or lime slurry pressure injection is hardly 38 to 50mm in 1 to 4 years unless extensive fissure and crack system is present. The hydration of Portland cement is a complex pozzolanic reaction that produces a variety of different compounds and gels. The results of mixing cement with clay soil are similar to that of lime. It reduces liquid limit, the plastic index and the potential of volume change, it increases the shrinkage limit and shear strength. For highly plastic clay, it is not effective like lime in stabilization. Addition of 2 to 6% cement content can produce a soil that acts as a semi rigid slab (John). Some investigators have tried and succeeded in minimizing the swelling of expansive soil using chemicals like calcium chloride (CaCl2), calcium sulfate (CaSo4), potassium chloride (Kcl), aluminum chloride (AlCl3), etc.

## Stabilization by Industrial Wastes

Utilization of industrial wastes like fly ash, quarry dust, silica fume, copper slag, tannery sludge, etc (Sabat et al, Stalin et al) in the geotechnical engineering field will solve the problem of disposal of these wastes. Extensive research is carried and carrying by the geotechnical investigators to reduce the swelling of expansive soils by using industrial wastes. Fly ash is a waste material produced due to burning of coal for thermal power industries. It is a hazardous material causing environmental pollution degradation. Fly ash is added to soils treated with lime to increase the pozzolanic reaction and improve the gradation of granular soils. The pozzolanic activity of silt soils has been improved by using a lime-fly ash ratio of 1:2. Liquid limit decreases and plastic limit increases with increase in the percentage of fly ash. Generally, the plasticity index reduces by about 50% when 20% of fly ash added. The optimum moisture content decreases and maximum dry unit weight increase with increase in fly ash content. When the non–plastic fly ash particles are added to the expansive clay the water content required for the reorientation of the particles will be less (Pandian et al., 2004).

## Stabilization by Reinforcement

Using fibers like jute fabrics, coir ropes, rubber tire chips, waste plastics, synthetic fibre etc can successfully stabilize the expansive soils. The work reported by Raid R. Al-Omari and Faris J. Hamodi (1991) showed the feasibility of using tensile geogrid for the purpose of controlling the swell of plastic soils. Swelling tests using an enlarged oedometer revealed promising results. The reinforcements were cylindrical geogrid of varying stiffness values embedded in clays of different plasticity indices. The reduction in swell increased with increasing the geogrid stiffness, apparently due to a strong ‘interference’ bond restricting the relative movement between clay and the grid. A footings model test confirmed the effectiveness of the proposed technique.

## Horizontal Moisture Barriers

Horizontal moisture barriers can be installed around buildings in the form of membranes or paving, both flexible and rigid. Horizontal barriers are meant to prevent excessive intake of moisture. Considerable success has been achieved with asphaltic membranes-catalytically blown asphalt membranes or prefabricated sheets. Asphalt membranes can be used to cover the surface of expansive soils so that non-expansive fill can be placed on top of the membranes. This minimizes infiltration of surface water into the under slab soils.

## Vertical Moisture Barriers

Vertical moisture barriers using concrete, ferrocement or any other impervious material around the perimeter of the building, to cut off the source of water, can be very useful in minimizing seasonal drying and shrinkage of the perimeter foundation soils and also in maintaining long-term uniform moisture conditions beneath covered areas. Vertical moisture barriers should be provided to a depth greater than the depth of seasonal moisture changes.

SERC Roorkee / Ghaziabad have developed technology for ferrocement waterproofing and water barriers. Construction and same has been successfully used in field. Distress in Lightly Loaded Structures Founded on Expansive Soils If the load is placed on the expansive soil is more, the selling is arrested. When the imposed loads are light, the swelling is more pronounced. It is interesting to note that it is rare that heavily loaded structures have problem with swelling soils while it is the lightly loaded single and two storeyed buildings which experience maximum distress.

## Causes for Distress in Lightly Loaded Structures

The following are the causes for distress in lightly loaded structures founded on expansive soils:

- The construction of building on marshy area and water table is observed at a shallow depth below the ground level.

- There is no flagging/plinth protection around the building.

- Growth of vegetation is observed around the building.

- Sump tank and sewage pipes are very close to the foundation.

- Wastewater and rainwater are disposed directly on the ground very close to the foundation.

- Cracks at plinth, sill, lintel levels and differential heaving of flooring, shifting of walls, extensive cracks are observed in internal and external walls of the building. It is due to the high swelling and shrinking characteristics of expansive black cotton soil in the foundation region.

- The presence of chloride and sulphate contents in fine aggregate are very high compared to the permissible values aggregate could have affect the concrete durability, which in turn have results severe corrosion of reinforcement in various members.

## Measures for Rehabilitation of Distressed Structures Founded on Expansive Soils

The following restoration measures as suggested below to counteract the dual problem of swelling and shrinking behavior of expansive clay (Rama Rao M, et al (2004), Sivapullaiah, et al (2005), Prabhakar, et al (2005):

- Construction of additional one or two floors above the existing building should be done so that the loading on the foundation would be more than the existing swelling pressure.

- The plinth beam should be separated from the natural ground by leaving an air gap of 8 to 10cm between the plinth beam bottom and natural ground. If the gap is not provided the plinth beam have at least to be designed for upward pressure due to soil swelling.

- A flexible water proof apron (plinth protection) of about width 2.0m shall be provided all round the building.

- Installation of horizontal/ vertical moisture barriers around the perimeter of the building.

- The internal non-load bearing walls with wide multiple cracks and dislocations shall be removing completely and rebuilt. Before dismantling, the complete roof should be supported by either steel or timber props.

- Flooring shall be redone after removing existing filled up soil up to about 1.5 m from the floor level and replacing the same with well-compacted non-expansive materials placed in layers not exceeding 30cm thickness.

- The sewer pipes with leak proof joints close to the foundation shall be beyond the foundation media.

- Providing sump tank far from foundation region.

- Plantation of trees, plants and hedges within 3m distance around the building should be avoided. This because of extensive watering of plants close to the building contributes to swelling.

- Discharging rainwater collected from roof at a distance from the structure.

## Fly Ash Cushion

Each one of the above methods has one limitation or the other, in terms of its efficacy or economy. The studies have been carried out using fly ash as a cushioning material (Sree Ramarao et al., 2005). Developments of cohesive bonds in a lime-stabilized fly ash cushion, when stabilized with lime, is expected to produce an environment similar to the one obtained in CNS material following saturation and consequently arrest heave. The results of the study showed a new solution to the problem heave of expansive soil in the form of “Fly ash cushion method.” It also solves the problem of fly ash utilization and disposal to some extent. If at a site containing black cotton soil, the depth of the active zone is 3m, it would be sufficient if 1.5m of expansive clay is removed and replaced with fly ash cushion to get the heave reduced significantly. With the superstructure load causing further reduction of heave, the amount of sub-excavation and replacement with lime stabilized fly ash cushion can be further reduced.

## Conclusion

Adequate geotechnical investigations are imperative for the characterization of expansive soil. By evaluating the properties of expansive soils accurately, it is feasible to choose the proper foundation technique with a good constriction quality. The distress in the lightly loaded structures is essentially due to high swelling and shrinking characteristics of expansive black cotton soil in the foundation media. The light loaded structures founded on expansive soils must be designed in such way to observe that the load coming on the structure is sufficiently more than the swelling pressure of the expansive soil. It should be ensured that there is no presence of high level of chloride and sulphate contents in fine aggregate using during construction, if not that may lead to the corrosion of reinforcement .

Failure case:

CASE HISTORY

- Background

Similar to Case History 1, this project was under construction when failures occurred. This project is also an access road with prestressed concrete bridge over a river in Sarawak. The proposed heights of the approach embankments on both sides of the abutments were about 5m with side slopes of 1v(vertical) to 1.5h(horizontal). These embankments were constructed over 25m thick of soft coastal and riverine alluvium clay followed by dense silty Sand and very stiff silty clay. The soft alluvium generally has SPT N’ value of zero and average moisture content of more than 70%. Fig. 11 shows the partially completed bridge after failure and removal of failed materials. The layout is shown in Fig and the subsoil profile

in shown in Fig.

Overview of partially completed bridge.

Layout of the Bridge in Case History

Subsoil condition

- In the construction drawings, the approach embankments using local fills were supported by 200x200mmRC piles with pilecaps. In addition, 6m length wood piles were also used between the RC piles forfurther support of the embankment fill. More wood piles were also installed on the banks of the rivertrying to stabilize the lateral displacement of the soft alluvium. The abutments and piers are generally supported by 400mm diameter spun piles.

- Slip Failures of the Approach Embankments

- A deep seated slip failure occurred at the approach embankment about 25m from Abutment II. It happened when the fill reached about 3m high. Fig. 14 shows the shear drop after removal of some of the fill near the abutment.

Shear Drop at about 25m from Tilted Abutment

- Abutment II has tilted away from the river with the magnitude of about 550mm at the top of the abutment at the time of the site inspection by the Authors who were carrying out geotechnical investigation of the failure. The tilt translates into an angular distortion of 1/6. Due to the excessive angular distortion, the integrity of the spun piles driven to set into the stiffer stratum has also been affected as it exceeds the normal threshold of about 1/75. Due to the tilt of the Abutment II away from Pier II, a gap of about 300mm wide was observed between the two bridge decks at the pier’s pile cap. Fig. 15 shows the photograph of the tilt at the Abutment II and the gap between two bridge decks. The failure also caused the pile cap at Pier II to tilt as shown in Fig. 16. Fig. 17 shows the schematic diagram of the possible slip plane relative to the deformed structures.

Tilted Abutment and Observed Gap between Bridge Decks

- These observations infer that the slip of the Approach Embankment near Abutment II is deep seated and is consistent with the depth of the soft alluvium. The cause of the rotational slip failure is due to the weak subsoil unable to support the weight of the approach embankment. The weight of embankment initiated the consolidation settlement of the soft subsoil and mobilized the low shear strength of the slip failure plane. The use of the 6m wood piles and RC piles offers little lateral resistance and instead, extends the rotational slip deeper into the soft subsoil. At the pier, the bridge decks, being simply supported and fixed to the abutment via bearing pad, had moved along with the displacement of the abutment.

Titled pilecap at Pier II

Schematic of the slip failure

- At the start of the construction, the contractor observed that their personnel could not walk on the riverbanks without their feet sinking into the soft subsoil to a depth of about a foot. This observation infers that the upper subsoil undrained shear strength of the subsoil is estimated at about 10 kPa. As preliminary check using correlation of 5*su to obtain ultimate bearing capacity of 50 to 60kPa, the estimated maximum height of fill that can be supported is about 3m which is consistent with the observed failure during embankment filling to 3m high. Therefore, if the designer and contractor had carried out simple checks, failure could have been prevented. Additional subsurface investigation after the failure shows that the undrained shear strength from the vane shear tests range from 18 kPa to 51 kPa with remoulded strength of 7 kPa to 12 kPa. The higher su obtained from the additional S.I. is due to the gain in strength during the whole period of filling.

- Remedial Measures:

- The rotational slip failure of the approach embankment is due to many factors such as inadequacy in the design, construction control, the soft subsoil and absence of adequate ground treatment.

- Several remedial options were explored for the embankment. The first remedial option is to remove the failed embankment fill and re-construct a new RC ramp (bridge) with ground beams for increased rigidity. This option avoids the weight of the fill bearing on the soft subsoil. The second option is to surcharge the soft subsoil in combination with prefabricated vertical drains to accelerate the consolidation process of the clayey subsoil and allow the subsoil to gain strength with time. The third option is to use piled embankment with slab to transfer the embankment load to the stiffer soil stratum instead of the soft upper clay.

- After much consideration by the client, the third option was chosen for the shortest construction time in order to put the bridge into service and no long term risk of further subsoil settlement. However, in this option, the soffit of the RC slab should be at or below the original ground level to avoid additional load on the soft upper subsoil stratum that can generate negative skin friction on both the abutment and embankment piles.

- At the tilted abutment, analyses of the pile head movement of the existing piles showed that integrity of the piles is doubtful and shall be compensated. However, there are two options of installing the compensation piles; firstly at the sides of the existing pile group and secondly, behind the abutment. The first option requires demolishing the existing abutment and enlarging the pilecap. The second option minimizes modification of the abutment but requires longer I-beams for support of the bridge deck. In addition, there is also a risk the compensation piles might be impeded by the wood and RC piles since the location of these piles might have displaced along with the slip failure.

- Option 1 was chosen for the minimal remedial cost by reusing the existing I-beams and minimizes risk of  the new spun piles striking the existing wooden and RC piles. For the pier foundation, the existing spun piles are fully compensated by demolishing the existing pier and pilecap and installing new ones at the sides. The total estimated cost of remedial works is about 1.3 million ringgit.

LESSONS LEARNED AND PREVENTIVE MEASURES

- From the two case histories presented in this paper, it is obvious that they are very similar in nature and can be categorized to be caused by the following factors:-

- Inadequacy of geotechnical design for the approach embankments or abutments.

- Lack of understanding of the subsoil condition and awareness on the possible problems/failure that could happen during construction.

- Lack of construction control and site supervision by the Consultant

- It is very obvious that the two failures are due to inadequacy of geotechnical design for the approach embankments and abutments. If proper geotechnical analyses and designs were carried out, the failures could have been prevented. The designs of approach the embankment and abutment are quite similar to normal fill embankment where key issues like stability and settlement shall be properly addressed. Although settlement calculation is equally important, they are not discussed here as it is not the main factor causing the failures but rather a long term serviceability problem that required regular maintenance.

- For embankment and abutment stability, both circular and non-circular (wedge) failure surfaces shall be evaluated using a limit equilibrium analysis (Tan & Gue, 2000). It is very common to wrongly assume that as long as the structural design of an abutment has considered both vertical and lateral pressures, slip failure would not occur. A good example of abutment instability is shown in Fig. 17 where a deep seated instability of the embankment fill behind the abutment seriously affect the stability of the abutment. The most critical condition that usually triggers failure is during filling where the stability of an embankment shall be analysed based on undrained shear strength (su) of the subsoil. The recommended Factor of Safety (FOS) against instability is at least 1.2 for short term. Long term stability is usually less critical as the subsoil increases its strength with time. The stability of embankments and abutments in long term shall be checked using effective stress strength parameters (c’ and f’) and the minimum FOS required is 1.4.

- A quick preliminary check on the stability of the embankment is possible using modified bearing capacity

- equation below :

qallow = (su. Nc / FOS)

where :

qallow      =      allowable bearing pressure  (gfill.H + 10) (kN/m2)

gfill            =       bulk unit weight of the compacted fill (kN/m3)

H                =       allowable height of embankment (m)

su               =        undrained shear strength of the subsoil (kPa)

Nc              =         5 (suggested by Authors for ease of hand calculation)

FOS            =          Factor of Safety

- Note : The 10kPa allowance in the qallow is to cater for traffic load.

- Design consultant, consultant’s site engineer(s) and contractor should have some fundamental geotechnical knowledge which include understanding of the subsoil condition and awareness on the possible problems or failures that could happen during construction. A good example is shown in Section 3.2 where the contractor were aware that their personnel could not walk on the very soft riverbank and could have used the simple bearing capacity equation to check the allowable height of the fill the subsoil can support. More often than not, failures were due to bad temporary works that were never considered for in the design. One serious problem that usually occurs for bridge project is the temporary fill placed by the contractor to form a temporary platform to facilitate their piling or other construction works. If not careful, slip failure in subsoil could be triggered by the load from the temporary fill. Therefore, it is recommended that the design consultant should consider the possible construction method to be used by the contractor and designed for it.

- The design consultant shall also ensure that during construction, the contractor must carry out works according to the approved method statement to prevent failure. It is also important for the design consultant to ensure the method statement including temporary works proposed by the contractor does not cause failure. Finally, the proper full-time site supervision by the consultant’s representatives with adequate site experiences and knowledge are also very important to prevent failure due to temporary works and ensure permanent works are constructed according to the drawings and specifications. Another common problem caused by temporary fill over soft ground is the failure to remove the temporary fill after construction. The temporary fill will cause the compressible subsoil to settle with  time (consolidation settlement). If this area has piles, then the piles will be subjected to down drag (negative skin friction) due to the settling subsoil and reduce the capacity of the piles. If the down drag is not catered for in the design, the piles will have lower allowable capacity and larger settlement causing distortion to the structures. Therefore, the design consultant shall ensure the removal of temporary fillafter construction by the contractor or to design the piles to accommodate negative skin friction.

- CONCLUSIONS:

- The success of bridge construction on soft ground relies on proper planning, analysis, design, construction control and site supervision. However, from the two case histories presented in this paper, it is obvious that they are very similar in nature and can be categorized to be caused by the following factors:-

- Inadequacy of geotechnical design for the approach embankments or abutments.

- Lack of understanding of the subsoil condition and awareness on the possible problems/failure that could happen during construction.

- Lack of construction control and site supervision by the Consultant

- To prevent embankment and abutment failure due to instability, both circular and non-circular (wedge) failure surfaces shall be checked using limit equilibrium analyses. A quick preliminary check on the stability of the embankment is possible using modified bearing capacity equation of

qallow = (su. Nc / FOS)

- It is also important for design consultant, consultant’s site representatives and contractor to have some fundamental geotechnical knowledge so that any irregularities at site can be spotted and precautionary actions carried out before failure occurs. Finally, proper full-time site supervision by the consultant’s representatives with adequate experiences and knowledge are also very important to prevent failure due to un-engineered temporary works

COMPACTION CHARACTERISTICS

Maximum dry density

The SP compaction showed an increase maximum dry density (Fig.1) with increasing dosage of GSA up to about 4% of GSA. The increase in the MDD is due to the flocculation and agglomeration leading to volumetric decrease in density (Medubi 1998).The decrease in MDD

initially for SP compaction was due to the presence of large, low density aggregate of particles (Osula, 1984).

Above 4 % GSA content there is a decrease in the MDD, this decrease could be as a result of the void within the coarse aggregate being filled with groundnut shell ash particles (Steven and Osinubi, 2006). This result is in conformity to the general trend and earlier findings

by Osinubi (1998), Marks and Harlibutton (1970).

However, above 6% GSA content there is a possibility that the formation of new compounds have occured which consequently lead to an increase in the MDD at 8% of GSA content with the general trend. The MDD for the WAS compactive effort is in conformity with the trend of decreasing OMC with increasing MDD. At specific ash contents, the results indicate a decrease in MDD with increasing GSA contents. The initial decrease in the MDD can be attributed to the replacement of the soil by the GSA which has lower specific gravity compared to that of the soil (Osinubi, 1996; Moses, 2008; Steven and Osinubi, 2007,). It may also be attributed to coating of the soil by the ash content which result to large particles with larger voids and hence less density (Osula, 1984; and, Ola, 1983).

The increase in density from the minimum attained value at 6% GSA contents to 8% GSA contents could be due to molecular rearrangement in the formation of “transitional compounds” which have high density at 8% GSA content (Osinubi, 1998a). - 421 - Optimum moisture content The variation of OMC with GSA of the SP, and WA energy levels are shown in Figs. 2. There was an initial increase in OMC with increase in GSA for the Standard Proctor and West African Standard compactive efforts. The initial increment could have been as a result of increasing demand for water by various cations and the clay mineral particles to undergo hydration reaction (Moses, 2008; Osinubi, 1997; Steven and Osinubi, 2006,). The subsequent decrease might have been due to cation exchange reaction that caused the flocculation of clay particles. For specimens compacted at the energy level of West African standard, the final decrease in

OMC recorded was probably due to self – desiccation in which all the water was used, resulting in low hydration. When no water movement to or from cement – paste permitted, the water is used up in the hydration reaction, until too little is left to saturate the solid surfaces and hence the relative humidity within the paste decreases. The process described above might have affected the

reaction mechanism of stabilized soil (Osinubi, 2000).

Optimum moisture content

The variation of OMC with GSA of the SP, and WA energy levels . There was an initial increase in OMC with increase in GSA for the Standard Proctor and West

African Standard compactive efforts. The initial increment could have been as a result of increasing demand for water by various cations and the clay mineral particles to undergo hydration reaction (Moses, 2008; Osinubi, 1997; Steven and Osinubi, 2006,). The subsequent decrease might have been due to cation exchange reaction that caused the flocculation of clay

particles. For specimens compacted at the energy level of West African standard, the final decrease in OMC recorded was probably due to self – desiccation in which all the water was used, resulting in low hydration. When no water movement to or from cement – paste permitted, the water is used up in the hydration reaction, until too little is left to saturate the solid surfaces and hence the

relative humidity within the paste decreases. The process described above might have affected the reaction mechanism of stabilized soil (Osinubi, 2000).
STRENGTH CHARACTERISTICS

Unconfined compressive strength

The main test recommended for use for determining required amount of additive to be used in the stabilization of soils is the unconfined compressive strength (UCS) test (Singh, 1991). The 7day UCS test results slight improvement with increasing compactive effort. The peak 7 days UCS value for the SP energy level is 455kN/m2 at 4% GSA content. This value fell short of 1710 kN/m2 specified by TRRL (1977) as criterion for adequate stabilization using OPC. The decrease in strength at higher groundnut shell ash content was as a result of insufficient water to bring the pozzolanic reaction to completion. The UCS at WA energy levels for the 7 days curing period had peak values of 526 kN/m2 at

6% GSA content. The trend of the UCS for the WAS compactive energy level shows a similarity. The values of UCS obtained failed to meet the recommendation by Iges and Metcalf (1972) for sub-base material.

The UCS at 14 days (Fig.4.) showed marked differences in values from one another and from that of the 7 days curing period for both SP and WA compactive effort . This indicates that GSA admixture has long time strength improving capability, which implies that the progressive

increase in strength will enhance the stability of the pavement. The peak 14 day UCS values for SP and WAS are 935kN/m2, and 542kN/m2 at 4 % and 6% GSA contents respectively. The peak values at 28 days curing (Fig.5.) period are 867 kN/m2 and 2253 kN/m2 at the energy levels of SP and WA with their GSA content being 4% for both.

DURABILITY

The durability assessment of specimen is normally in such a manner as to simulate some of the worst conditions that can be attained in the field for any soil to be used for engineering purposes, immersion of the cured specimen in water before testing its compressive strength is employed to ensure that the stabilized material do not fail under adverse field conditions. The values obtained under these conditions are analyzed in conjunction with the 14 days curing period UCS test results. Cured specimens are normally soaked for 7 days before testing to obtain the percentage resistance to loss in strength of the stabilized material as recommended for tropical

countries by Ola (1974).
CONCLUSIONS

The natural black cotton soil was classified as A – 7 – 6 or CL in the AASHTO and Unified Soil Classification System (USCS), respectively. Soils under these groups are of poor engineering benefit. Treatment of natural the soil with Groundnut shell ash gave a peak 7 day UCS value at SP of 455kN/m2 at 4% GSA content and 526kN/m2 at 6% GSA content for WA compactive effort. This value fell short of 1710 kN/m2 specified by TRRL (1977) for base materials stabilization using

OPC. And they fell to meet the requirement of 687–1373 kN/m2 for sub-base as specified by Ingles and Metcalf (1972). The peak soaked CBR values of 4 % at SP and 4% at WA were attained at 6 % (GSA) and 0% (GSA) respectively. These values fell to satisfy the specification for base and sub-base materials as recommended by the Nigerian General Specifications (1997). Finally, the durability assessments of sample failed to meet the acceptable requirement.

FOUNDATIONS:

1 For classification of strata in excavation refer notes given in chapter R-3. Excavation shall be taken to the width of the lowest step of the footing and the sides shall be left plumb where the nature of soil allows it. Where the nature of soil or the depth of, the trench and season of the year do not permit vertical sides. Necessary steps shall be taken for shoring strutting and planking or cut slopes to a safer angle or both with due regard to the safety of personnel and works. Propping shall be 'undertaken when any foundations or stressed zone from an adjoining structure is within a line of 1 vertical to 2 horizontal from the bottom of the excavation.

2 Open Foundation shall be constucted in dry condition and the contractor shall provide for

dewatering arrangement to the satisfaction of the engineer. Where water is met with in excavation due to springs, seepage, or by other reasons steps shall be taken for bailing/pumping out water, construction of diversion channels, bunds, cofferdams and other necessary works to keep the foundation trenches when so required where cofferdams are required, these shall be carried to adequate depths and heights, be safely designed and constructed and be made as watertight as is necessary for facilitating construction to be carried out inside them. If it is determinted beforehand that the foundations cannot be laid dry or the situation is found that the percolation is too heavy for keeping the foundation dry, the foundation concrete shall be laid under water by tremie pipe only. In case of flowing water or artesian springs, the flow shall be

stopped or reduced as far as possible at the time of concreting.

3 When foundation piles are used, the excavation of each pit shall be substantially completed before

beginning pile-driving operations therein. After pile driving operations in a given pit are completed,

all loose and displaced materials therein shall be removed to the elevation of the bottom of the

footings.

(i) The complete sub-surface investigation of strata in which pile foundations are proposed shall be

carried out in advance and by in-situ pile tests.

(ii) Reinforcement shall be provided as per design

(iii) Cement

For cement refer general instructions of the SOR

(iv) Fine aggregate

Fine aggregate shall consist of natural sand, crushed stone sand, crushed gravel sand stone dust. Aggregate most of which passes through 4.75 mm IS sieve is known as fine aggregate.

(v) Coarse Aggregate

For termite concreting, coarse aggregate having nominal size more than 20 mm should not be

used. Natural rounded shingle of appropriate size may also be used as coarse aggregate. It helps

to give high slump with less water cement ratio.

(vi) The placing of concrete shall be a continuous process from the toe level to the top of the pile.

To prevent segregation a tube or termie pipe as appropriate shall be used to place concrete in all

piles.

(vii) To ensure compaction by hydraulic static heads, rate of placing concrete in the pile shaft shall

not be less than 6 m (length of pile) per hour.

4 Pile Cap

Caps shall be of reinforced concrete. A minimum offset of 150 mm shall be provided beyond the

outer faces of the outer most piles in the group. If the pile cap is in contact with earth at the bottom,

a levelling course of minimum 100 mm thickness of M 15 nominal mix concrete shall be provided.

5 A temporary bench mark shall also be established near the well foundation, away from the zones of

blow-ups or possible settlement. The bench mark shall be checked regularly with respect to the

permanent bench mark established at the bridge site.

6 The well shall as far as possible be sunk true and vertical through all types of strata.

Sinking or loading of the well with kentlege shall be commenced only after the steining has been

cured for at least 48 hours or as specified in the drawings.

7 No well shall be permitted to be place in pre-dredged hole.

8 The well shall be sunk by excavating material uniformly from inside the dredge shole. Use of water

jetting, expolsives and divers may be adopted for sinking of wells through difficult strata with prior

approval of the Engineer.

9 Normally dewatering of well should not be permitted as a means for sinking the well. It also shall never be resorted to if there is any danager of sand blowing under the well. Dewatering shall however be have to be done when well is to be founded into rock. Pneumatic sinking may have to be resorted to where obstacles such as tree trunks, large size boulders, etc. are met at the bottom or when there is hard strata which cannot be removed by open dredging. The necessity for pneumatic sinking shall be decided by the Engineer.

10 Tolerances in well sinking

The permissible tilt and shift shall not exceed 1 (horizontal) in 80 (vertical) and the shift at the well

base shall not be more than 150 mm in any resultant direction. For the well steining and well cap the permissible tolerances shall be as follows :

(a) Variation in dimensions : + 50 mm - 10 mm

(b) Misplacement from speicified position in plan : 15 mm

(c) Surface irregularities measured with 3 m straight edge : 5 mm

(d) Variation of levels at the top : ± 25 mm

84

11 MEASUREMENT OF WELL FOUNDATION

(i) The cutting edge shall be measured in tonnes based on the net weight of metal used in it.

(ii) The concrete in curb, well steining and well cap shall be measured in cubic meters in each of the

items. The reinforcements shall be measured in tonnes separately in each of the items.

(iii) The measurement for well sinking shall be made in running meters for different depths and in

different types of strata (for example, predominantly sand/clay soil, soft rock, hard rock, etc) as

specified in the drawing. The depth of sinking shall be measured from the level specified in the

drawing. If no level has beeen specified in the appoved drawing, sinking shall be measured from the low water level or from the level at which the cutting edge was laid, whichever is higher.

(iv) The quantity of concrete in bottom and top plug shall be measured in cubic meters.

(v) The quantity of sand filling shall be measured in cubic meters.

(vi) Pneumatic sinking, where required shall be paid as a seprate item and shall be measured in

cubic meters of material to be excavated.

12 MEASUREMENT OF PILE FOUNDATION

Dimension shall be measured nearest to a cm. Measurement of length on completion shall be along

the axis of pile and shall be measured from top of shoe to the bottom of pile cap.

# Foundation Practices & Rehabilitation of Structures on Expansive Soils

## Introduction

Expansive soil is commonly known as black cotton soils, because of their color and their suitability for growing cotton. Black cotton soil is one of the major regional soil deposits in India, covering an area of about 3.0 lakh sq.km. Expansive soils are problematic soils because of their inherent potential to undergo volume changes corresponding to changes in the moisture regime. When they imbibe water during monsoon, they expand and on evaporation there of in summer, they shrink. Because of this alternate swelling and shrinkage, structures founded on them are severally damaged. The annul cost of damage to the civil engineering structures is estimated at £150 million in the UK, $1000 million in the USA and many billion of pounds worldwide (Gourley et al. 1993).
In India, black cotton soils have liquid limit values ranging from 50 to 100%, plasticity index ranging from 20 to 65% and shrinkage limit from 9 to 14%. The amount of swell generally increases with increase in the plasticity index. The swelling potential depends on the type of clay mineral, crystal lattice structure, cation exchange capacity, ability of water absorption, density and water content. Swell in the vertical direction is called heave. Among the illite, kaolinite and montmorillinite clay minerals, the montmorillinite possesses the greatest ability to swell by illite. The Kaolinite does not swell. Black cotton soils are very hard in dry state and possess high bearing capacity. In summer, it is very common to see shrinkage cracks with hexagonal columnar structure, with vertical cracks as wide as 10mm extending up to a depth of 3m or more. Soils containing expansive clays become very sticky when wet and usually are characterized by surface cracks or a “popcorn” texture (Fig.1) when dry. Therefore, the presence of surface cracks (Fig.2) is usually an indication of an expansive soil.

Expansive soil with “popcorn” texture

## Problems With Expansive Soils

The problem is more in case of light structures; those cannot counteract the upward thrust posed by expansive soils. The damage will be apparent, usually, several years after construction. The soil below will exert swelling pressure both upwards and laterally. As a result, the floor slab is lifted up, leading to cracking of floor. Cracking is normally evident at the corners of window and door openings. These usually assume in the form of diagonal cracks-a consequence of differential settlement in the wall (Fig. 3 & 4). Often, utilities buried in soil as the water pipelines and sewage lines, get damaged due to displacement in the soil in which they are buried. The ensuing leakage further aggravate the situation. Roads that pass through expansive soil sub-grade are subjected to heaving and shrinkage settlement of these treacherous soils. Both the lined and unlined canals are subjected to the vagaries of expansive soils. The unlined canal slopes erode and become soft. Canal beds heave up obstructing the functioning of the canal. The concrete linings splinter like glass pieces on account of deleterious cyclic movement of background swelling clay. This heavy results in seepage losses.

## Deep Foundation Techniques

In this case, the foundation is made to rest at some depth by passing the soil in the active zone, i.e. the zone within which volume changes in the soil occur due to seasonal moisture changes.

The maximum spans up to which a particular type of bridge

can be recommended.

1 RCC arch bridge 200 m

2 RCC bow-string girder bridge 45 m

3 RCC cantilever bridges with balanced type 30 m

4 RCC continuous bridge 45 m

5 RCC deck type girder bridge 20 m

6 RCC filled spandrel fixed arch bridge 35 m

7 RCC open spandrel rib type bridge 60 m

8 RCC portal frame bridge 15 m

9 Prestressed concrete arch bridge 150 m

10 Prestressed concrete continuous bridge 110 m

11 Prestressed concrete girder bridge simply

Supported 55 m

12 Steel arch bridge 500 m

13 Steel bow-string girder bridge 240 m

14 Steel cable suspension bridge 1200 m

15 Steel plate girder 30 m

16 Steel rolled beam bridge 10 m

17 Steel truss bridge 180 m

Design and scope as per Agreement :-

- Sub Structure - RCC open foundation

ii) Super Structure - Single lane suitable RCC bridge with RCC decking as

per IRC – 40 R loading.

- Protection work - Wing wall as per relevant IRC code.

2) Design of various structural components of bridge and detailed  structural drawings.

3) Preparation of detailed project report based on above data separately for suitable loading capacity of RCC bridge.

4) All design calculation should be confirmed to relevant I.S. code.

5) The detailed project report and bill of quantities neatly printed in single side shall be submitted in triplicate.

INTRODUCTION TO WORK

1 DESIGN OF SUBSTRUCTURE

COMPONENTS OF ELEVATED VIADUCT

UNDER PHASE II OF DELHI MRTS

PROJECT.

2 DESIGN OF S/S OF ROB CROSSING ON

INDORE-KHALGHAT SECTION ON NH-3

DESIGN OF SUBSTRUCTURE

COMPONENTS INCLUDES

CALCULATION OF BEARING LOADS

DESIGN OF PORTAL PIER AND FOUNDATION

ELEVATION

BEARING LOAD CALCULATIONS

I. CALCULATE REACTIONS DUE TO                                                                                                                          SELF

WEIGHT,SIDL & LL

II. CALCULATE ECCENTRICITY DUE TO

CURVATURE,IF ANY,BY -

2/3*RADIUS*(1-COSO)

III. CALCULATE MOMENT DUE TO

ECCENTRICITY

IV. FIND OUT MOMENT DUE TO

ECCENTRICITY DUE TO ONE TRACK

LOADED

BEARING LOAD CALCULATIONS

i. SEISMIC FORCE ( as per IRC 6:2000)

a) SEISMIC TRANSVERSE FORCE

(DL,SIDL,25%LL)

b) SEISMIC VERTICAL FORCE

(DL,SIDL,50%LL)

BEARING LOAD CALCULATIONS

 FIND OUT CENTRIFUGAL FORCE(CF) BY:-

LOAD*V2/(127*R)

 CALCULATE MOMENT DUE TO ‘CF’

 MAX & MIN BEARING LOAD

= vertical reaction } moment no. of bearings bearing spacing

DESIGN OF PORTAL PIER & OPEN FOUNDATION

DESIGN OF PORTAL PIER & OPEN FOUNDATION

i. LOAD

CALCULATIONS

DESIGN OF PORTAL PIER & OPEN FOUNDATION

i. FORCES CALCULATED AS EXPLAINED ARE

APPLIED ON THE IDEALISED STRUCTURE

IN STAAD-PRO

ii. FROM STAAD,FORCES ARE CALCULATED

ON FOUNDATION TOP

iii. CRITICAL LOAD CASES ARE MADE FOR

DESIGN OF FOOTING

DESIGN OF PORTAL PIER & OPEN FOUNDATION

i. SIZE OF FOOTING IS CHECKED WITH THE

HELP OF LABFIL SOFTWARE (house built software)

DESIGN OF PORTAL PIER & OPEN FOUNDATION

i. FOOTING SIZE IS CHECKED FOR BASE

PRESSURE

ii. FOOTING DEPTH IS CHECKED FOR SHEAR

AND REINFORCEMENT IS CALCULATED

CORRESSPONDING TO BENDING MOMENT

DESIGN OF PORTAL PIER & OPEN FOUNDATION

i. PIER SHAFTS ARE ALSO DESIGNED BY

USING LABFIL SOFTWARE

ii. FORCES ON TOP OF THE PIER ARE

CALCULATED FROM STAAD

iii. IDEALISATION OF PIER IS MADE AND

REINFORCEMENT IS PROVIDED

DESIGN OF PORTAL PIER & OPEN FOUNDATION

i. THEN BY LABFIL , STRESSES ARE WORKED

OUT WHICH SHOULD BE LESS THAN

PERMISSIBLE.

LOAD CALCULATION

 DL

 SIDL

 LL (70R & CLASS A LOADING)

GRID IDEALISATION

Groundnut Shell Ash Stabilization of

Black Cotton Soil.

The safe disposal of industrial and agricultural waste products demands urgent and cost effective solutions because of the debilitating effect of these materials on the environment and to the health hazards that these wastes constitute.

In order to make deficient soils useful and meet geotechnical engineering design requirements researchers (Osinubi, 1997; 2000a,b; Moses, 2008; Alhassan and Mustapha, 2007;

Osinubi and Medubi, 1998; Medjo and Riskowiski, 2004; Osinubi and Eberemu, 2005; Osinubi and Stephen, 2006; Osinubi et al., 2007a,b; Osinubi et al., 2008a,b; Osinubi and Eberemu, 2009b; Osinubi et.al., 2009) have focused more on the use of potentially cost effective materials that are

locally available from industrial and agricultural waste in order to improve the properties of deficient soils.

The over dependence on industrially manufactured soil improving additives (cement, lime etc) have kept the cost of construction of stabilized road financially high. This hitherto have continued to deter the underdeveloped and poor nations of the world from providing accessible roads to meet the need of their rural dwellers who constitute large percentage of their population which are mostly rural farmers. Furthermore, the World Bank has been expending substantial amount of money on research aimed at harnessing industrial waste products for further usage. Thus, the possible use of agricultural waste (such as Groundnut Shell Ash - GSA) will considerably reduce the cost of construction and as well as reduce or eliminate the environmental hazards caused by such waste. Groundnut shell is an agricultural waste obtained from milling of groundnut. Nigeria contributes about 7 percent of world groundnut production which makes Nigeria the 3rd largest producer of groundnut in the world. In 2002, about 2,699,000 Mt of

groundnut were produced in about 2,783,000 Hectares of Land. Meanwhile, the ash from groundnut shell has been categorized under pozzolana (Alabadan et.al, 2006), with about 8.66%

Calcium Oxide (CaO), 1.93% Iron Oxide (Fe2o3), 6.12% Magnesium Oxide (MgO), 15.92% Silicon Oxide (SiO2), and 6.73% Aluminum Oxide (Al2O3). The utilization of this pozzola as a replacement for traditional stabilizers will go a long way in actualizing the dreams of most developing countries of scouting for cheap and readily available construction materials. Groundnut shell ash has been used in concrete as a partial replacement material for cement with a

measure of success achieved (Alabadan et al., 2005).

Problematic soils such as expansive soils are normally encountered in foundation engineering designs for highways, embankments, retaining walls, backfills etc. Expansive soils are normally found in semi – arid regions of tropical and temperate climate zones and are abundant, where the annual evaporation exceeds the precipitation and can be found anywhere in the world (Chen, 1975; Warren and Kirby; 2004).

Expansive soils are also referred to as “black cotton soil” in some parts of the world. They are so named because of their suitability for growing cotton. Black cotton soils have varying colors’ ranging from light grey to dark grey and black. The mineralogy of this soil is dominated by the presence of montmorillonite which is characterized by large volume change from wet to dry seasons and vice versa. Deposits of black cotton soil in the field show a general pattern of cracks

during the dry season of the year. Cracks measuring 70 mm wide and over 1 m deep have been observed and may extend up to 3m or more in case of high deposits (Adeniji, 1991).The three most commonly used stabilizer for expansive clays are; bitumen; lime, and cement. Researchers (Ola,1983; Balogun,1991 and Osinubi,1995) attempted to stabilize this soil have reported that the stabilization of this soil with bitumen: lime or cement is effective. Unfortunately, the costs of these stabilizers are on the high side making them economically unattractive as stabilizing agents. Recent trend in research works in the field of geotechnical engineering and

construction materials (Osinubi, 1997; Osinubi, 2000a,b; Cokca, 2001; Medjo and Riskowski, 2004; 2000a,b; Moses, 2008; Osinubi and Medubi, 1997; Medjo and Riskowiski, 2004; Osinubi and Eberemu, 2005; Osinubi and Stephen, 2006; Osinubi et al., 2007a,b; Osinubi et al., 2008a,b;

Osinubi and Eberemu, 2009b; Osinubi et al., 2009) focuses more on the search for cheap and locally available materials such as bagasse ash, fly ash, blast furnace slag e.t.c. as stabilizing agents for the purpose of full or partially replacement of traditional stabilizers. Agricultural waste

is increasingly becoming a focus of researchers because of the enhanced pozzolanic capabilities of such waste when oxidized by burning. Thus, this study is aimed at evaluating the possibility of utilizing groundnut shell ash (GSA)

in the stabilization of black cotton soils.

LOCATION OF STUDY AREA

The soil used in this study is black cotton soil (light grey in colour) obtained along Gombe – Biu road in Yamatu Deba Local Government Area of Gombe State using the method of disturbed sampling. The location lies within latitude 10° 19’N and longitude 11° 30’E. In terms of extent of deposit, black cotton clays are not restricted to the area of study but are wide spread through out the north – eastern Nigeria. While the groundnut shell were obtained and ashed in open air under normal temperature in Zaria, Kaduna State of Nigeria.

Conclusions

The project   is   limited to the design of foundation,pier  and abutment considering  in  the black cotton soil. which have very dangerous behavior and as such we have taken depth of foundation as depth from H.F.L to the depth of foundation we have taken the remedial measure to project to the foundation  against sliding ,overturning so that it’s should be stable . we have made study of failure of bridges all around the world. precautions measure they have suggested that is also taken in consideration. It is a live project Constructed at parab haldaru kamrej   , surat. No doubt they have considered same is suggested in this project . So the bridge will be a stable.

REFERENCES

- Concrete Bridge Practical.

- Bridge Engineering (Rangwala’s Book)

- Site of Akshay Construction,Surat

- www.wikipedia.com

- www.Google.com

Guided by :

- MR. V.P.LUNJA ( PRINCIPAL)

- MR. R.D.PATEL ( LECTURER)

- MR. S.P.PATEL ( SITE ENGINEER)